## Slide 1
TUM HUMAN SPACEFLIGHT TECHNOLOGY
SPHERE
Thermal Insulation Laboratory
A classroom experiment linking transient heat transfer, physical testing and model validation
FINAL PROJECT PRESENTATION
Piyath Vithanage · Elio Krollpfeiffer
Dilan Fernando · Nuhansee Migelhewage
9 September 2026
Notes: Suggested timing: 0:30
Open with the project purpose: SPHERE turns a spacesuit thermal-control challenge into a measurable classroom experiment. Introduce the four-person team and preview the link between theory, the physical test, and Mission Control.
Handoff cue: Pause for the next speaker or section when the final point lands.
Sources:
- README.md
- output/pdf/SPHERE_Thermal_Insulation_Project_Report_Updated.pdf

## Slide 2
FINAL PRESENTATION
From spacesuit thermal control to a classroom experiment
SPHERE THERMAL INSULATION LABORATORY
02
THE ENGINEERING QUESTION
How do layered materials change the transient cooling of a protected thermal mass?
Warm water represents the protected thermal mass.
An ice-water bath supplies a repeatable cold boundary.
Four insulation builds create a controlled comparison.
Prediction and observation meet in the same workflow.
Analogy to spacecraft thermal control, not a vacuum simulation
Notes: Suggested timing: 0:45
Frame the laboratory as an engineering analogy. The ice bath emphasizes conduction and convection, while a real spacesuit in vacuum relies heavily on radiation control and active thermal management. Avoid claiming that the setup reproduces space.
Handoff cue: Pause for the next speaker or section when the final point lands.
Sources:
- Engineering Project Report, Sections 1 and 2
- SPHERE Mission Control overview

## Slide 3
FINAL PRESENTATION
One project connects experiment, software and assessment
SPHERE THERMAL INSULATION LABORATORY
03
DELIVERABLE SUITE
Mission Control browser application
Student and teacher manuals
Illustrated experimental SOP
Two-page task sheet
Revision flashcards
Unified ten-question assessment
The same settings and terminology now appear across every learning resource.
Notes: Suggested timing: 0:45
Explain that the strongest project outcome is integration. Students move from theory to assembly, prediction, measurement, analysis and assessment without changing tools or terminology.
Handoff cue: Pause for the next speaker or section when the final point lands.
Sources:
- README.md
- index.html
- student_manual.html
- teacher_manual.html

## Slide 4
FINAL PRESENTATION
Learning objectives and classroom constraints
SPHERE THERMAL INSULATION LABORATORY
04
01
Heat-transfer mechanisms
Distinguish conduction, convection and radiation in the test system.
02
Newton cooling model
Interpret the effective cooling constant and calculate a reference curve.
03
Experimental evidence
Collect a controlled 16-point temperature history and plot it.
04
Model evaluation
Use residuals and MAE to explain agreement and uncertainty.
Class format
Four groups in parallel · 55–70 minutes · 15-minute measurement interval · Reusable hardware
Notes: Suggested timing: 0:40
Connect each learning objective to an observable student action. The complete classroom run takes about 55 to 70 minutes, although the final presentation summarizes it in under 15 minutes.
Handoff cue: Pause for the next speaker or section when the final point lands.
Sources:
- README.md
- Engineering Project Report, Section 1

## Slide 5
FINAL PRESENTATION
Experimental hardware and boundary conditions
SPHERE THERMAL INSULATION LABORATORY
05
VERIFIED SETTINGS
100 mL
wide-mouth glass thermal core
≈80 °C
initial water temperature; record actual T₀
Measured
ice-water bath temperature Tenv
1 minute
sampling from t = 0 through 15
Four matched cores allow parallel classroom testing
Notes: Suggested timing: 0:45
Point out the separate bath probe, the centered core probe and the need for consistent immersion depth. The apparatus is deliberately simple, reusable and browser-independent at the sensing stage.
Handoff cue: Pause for the next speaker or section when the final point lands.
Sources:
- Engineering Project Report, Sections 3 and 10
- Thermal_Insulation_SOP.docx

## Slide 6
FINAL PRESENTATION
Four controlled insulation configurations
SPHERE THERMAL INSULATION LABORATORY
06
Bare control
k = 0.150 min⁻¹
Reference heat loss
Bubble wrap
k = 0.040 min⁻¹
Trapped air cells
Mylar only
k = 0.121 min⁻¹
Reflective layer
Full MLI
k = 0.015 min⁻¹
Cotton + bubble + Mylar
Reference coefficients are educational system settings, not material conductivities.
Notes: Suggested timing: 0:50
Describe the physical construction and keep the distinction between effective system coefficient k and material thermal conductivity λ. The current verified Mylar setting is 0.121 min⁻¹.
Handoff cue: Pause for the next speaker or section when the final point lands.
Sources:
- app.js, modelConstants
- Student Manual, test configurations
- Engineering Project Report, Section 3

## Slide 7
FINAL PRESENTATION
Thermodynamic framework
SPHERE THERMAL INSULATION LABORATORY
07
Newton cooling model
T(t) = Tenv + (T₀ − Tenv)e⁻ᵏᵗ
Smaller k means slower approach to the bath temperature
CONDUCTION
Direct contact through glass, water and solid layers
Cotton and interfaces add resistance
CONVECTION
Fluid movement in the bath and gaps
Sealed bubble cells restrict circulation
RADIATION
Infrared exchange between surfaces
Mylar reduces radiative exchange
Notes: Suggested timing: 1:00
Explain the model as a lumped-parameter approximation. The effective k captures geometry, thermal mass, the boundary and every heat-loss path. It must not be presented as the thermal conductivity of cotton, bubble wrap or Mylar.
Handoff cue: Pause for the next speaker or section when the final point lands.
Sources:
- Engineering Project Report, Section 2
- README.md, Engineering model

## Slide 8
FINAL PRESENTATION
Controlled method and safety-critical checks
SPHERE THERMAL INSULATION LABORATORY
08
01
PREPARE
Measure Tenv, label conditions, leak-test the cores
02
CONDITION
Fill 100 mL near 80 °C and record the actual T₀
03
MEASURE
Immerse consistently and log one reading each minute
04
ANALYSE
Compare curves, residuals, k and MAE
FAIR-TEST CONTROLS
Same jar geometry, water volume, probe depth and immersion location
Same sampling interval and documented starting-temperature tolerance
Rank unequal starts by temperature drop, normalized retention or fitted k
MANDATORY SAFETY
Adult handling of water near 80 °C; never use boiling water
Eye protection and heat-resistant gloves or tongs
Stable bath below waist height; electronics stay dry
Stop for leakage, probe movement or wet insulation
Notes: Suggested timing: 1:00
Present safety as a design requirement. An adult handles hot water, every capsule is leak-tested, and only the metal probe enters water. Mention that the appendix contains the complete 12-step procedure.
Handoff cue: Pause for the next speaker or section when the final point lands.
Sources:
- Engineering Project Report, Sections 4 and 10
- Thermal Insulation SOP, Safety and Control Requirements

## Slide 9
FINAL PRESENTATION
Mission Control links prediction with measurement
SPHERE THERMAL INSULATION LABORATORY
09
1
Select a configuration
Load its reference k value.
2
Set the boundary
Enter measured T₀ and Tenv.
3
Generate the prediction
Create a 0–15 minute cooling curve.
4
Enter observations
Overlay telemetry and calculate MAE.
Manual entry keeps the student involved in the act of measurement.
Notes: Suggested timing: 0:50
Explain the closed loop. The website calculates the model but does not automate the thermometer. Students still observe and enter every value, then receive immediate visual and numerical feedback.
Handoff cue: Pause for the next speaker or section when the final point lands.
Sources:
- index.html
- app.js
- Engineering Project Report, Section 6

## Slide 10
FINAL PRESENTATION
Live demonstration: prediction to evaluation
SPHERE THERMAL INSULATION LABORATORY
10
1
Choose Full MLI and confirm k = 0.015 min⁻¹
2
Run the 80 °C / 0 °C / 15 min prediction
3
Open Measurements and show the worked telemetry overlay
4
Read the 0.98 °C MAE and discuss one residual
If the browser or CDN assets fail, present these two verified screenshots and continue.
Notes: Suggested timing: 2:00–3:00
DEMO SCRIPT
1. Open Simulator. Select Multilayer assembly. Confirm T₀ = 80 °C, Tenv = 0 °C and 15 minutes.
2. Run the model and point to T(15) = 63.9 °C.
3. Open Measurements. Load or show the supplied full-MLI series. Point to 16/16 points and MAE = 0.98 °C.
4. Explain that residuals change sign because the measured curve does not follow one perfect exponential.
Fallback: remain on this slide if Chart.js, KaTeX or web fonts do not load. The screenshots preserve the exact demonstration state.
Handoff cue: Pause for the next speaker or section when the final point lands.
Sources:
- SPHERE Mission Control local website
- Worked telemetry from Engineering Project Report, Section 8

## Slide 11
FINAL PRESENTATION
Reference model separates the four expected cooling rates
SPHERE THERMAL INSULATION LABORATORY
11
Chart: Time (minutes)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Bare control | 80 | 68.86 | 59.27 | 51.01 | 43.9 | 37.79 | 32.53 | 28 | 24.1 | 20.74 | 17.85 | 15.36 | 13.22 | 11.38 | 9.8 | 8.43
Bubble wrap | 80 | 76.86 | 73.85 | 70.95 | 68.17 | 65.5 | 62.93 | 60.46 | 58.09 | 55.81 | 53.63 | 51.52 | 49.5 | 47.56 | 45.7 | 43.9
Mylar only | 80 | 70.88 | 62.8 | 55.65 | 49.31 | 43.69 | 38.71 | 34.3 | 30.39 | 26.92 | 23.86 | 21.14 | 18.73 | 16.59 | 14.7 | 13.03
Full MLI | 80 | 78.81 | 77.64 | 76.48 | 75.34 | 74.22 | 73.11 | 72.03 | 70.95 | 69.9 | 68.86 | 67.83 | 66.82 | 65.83 | 64.85 | 63.88
MODEL T₁₅
Bare
8.4 °C
Bubble
43.9 °C
Mylar
13.0 °C
Full MLI
63.9 °C
Assumptions: T₀ = 80 °C and Tenv = 0 °C
Notes: Suggested timing: 0:55
Use the chart to establish the expected ranking under one common starting point and boundary. State clearly that the coefficients are teaching references that require calibration for a new geometry or build.
Handoff cue: Pause for the next speaker or section when the final point lands.
Sources:
- app.js, modelConstants
- Engineering Project Report, Section 7

## Slide 12
FINAL PRESENTATION
The worked example shows the full MLI retaining the most heat
SPHERE THERMAL INSULATION LABORATORY
12
Chart: Time (minutes)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Full MLI | 77.6 | 76.6 | 76.1 | 75.6 | 75.1 | 74.5 | 73.9 | 73.5 | 72.1 | 70.6 | 69.7 | 68.5 | 67.4 | 65.8 | 64.1 | 62.7
Bubble wrap | 82.6 | 79 | 75.2 | 72.5 | 70 | 67.9 | 65.6 | 64 | 62.3 | 60.6 | 58.9 | 57.5 | 56.1 | 54.8 | 53.7 | 52.6
Bare control | 80.1 | 73.9 | 66 | 59.9 | 54.5 | 50.1 | 47.1 | 44.6 | 42.5 | 40.9 | 39.5 | 38.2 | 37.3 | 36.5 | 35.8 | 35.2
Mylar only | 80.5 | 68.6 | 61.8 | 55.8 | 51.3 | 47.8 | 44.9 | 42.5 | 40.6 | 38.9 | 38.1 | 36.3 | 35.5 | 34.6 | 33.9 | 33.3
Full MLI
14.9 °C drop
74.1% retained
Bubble
30.0 °C drop
52.1% retained
Bare
44.9 °C drop
25.3% retained
Mylar
47.2 °C drop
22.0% retained
Worked example only. Repeated measurements are required for validation.
Notes: Suggested timing: 1:10
Compare temperature drop rather than final temperature alone because the four trials started at different values. The full MLI produced the smallest drop. Bubble wrap ranked second. The example is illustrative and does not replace repeated trials.
Handoff cue: Pause for the next speaker or section when the final point lands.
Sources:
- Engineering Project Report, Section 8
- Thermal Insulation SOP, complete observed series

## Slide 13
FINAL PRESENTATION
Boundary conditions explain the weak Mylar-only result
SPHERE THERMAL INSULATION LABORATORY
13
WHAT THE DATA SUPPORT
The layered package produced the smallest measured temperature drop.
Bubble wrap provided useful resistance through intact air cells.
The observed Mylar curve strongly disagreed with its reference model.
WHY MYLAR CAN FAIL HERE
Reflective foil targets infrared exchange, which matters strongly in vacuum.
Direct liquid contact and leakage can dominate the classroom water bath.
One weak run does not prove reflective insulation is ineffective in space.
Main uncertainties: probe position, neck seal, thermal stratification, bath warming, immersion depth and layer compression
Notes: Suggested timing: 1:00
Use the Mylar result to demonstrate engineering interpretation. The correct conclusion concerns the boundary and construction, not a universal property of reflective insulation. Name two or three uncertainty sources and explain their direction of influence.
Handoff cue: Pause for the next speaker or section when the final point lands.
Sources:
- Engineering Project Report, Section 9

## Slide 14
FINAL PRESENTATION
SPHERE delivers a complete theory-to-evidence learning loop
SPHERE THERMAL INSULATION LABORATORY
14
PROJECT OUTCOME
Students predict, build, measure and critique the same thermal system.
Aligned website, manuals, SOP, worksheet and assessment
Reusable apparatus with no native software installation
Clear separation between teaching models and measured evidence
CONTRIBUTIONS
Piyath Vithanage
Website, integration, model and telemetry graphs, data visualisation
Dilan Fernando
Thermodynamics, experiment, analysis, documentation and project integration
Elio Krollpfeiffer and Nuhansee Migelhewage remain listed as project team members in the current repository and learning materials.
Notes: Suggested timing: 0:50
Close on the integration outcome. State the current contribution attribution exactly as documented. Invite questions on the experiment, model, website or classroom implementation.
Handoff cue: Pause for the next speaker or section when the final point lands.
Sources:
- Engineering Project Report, Sections 11 and 12
- README.md

## Slide 15
APPENDIX
Appendix: complete apparatus list
SPHERE THERMAL INSULATION LABORATORY
15
Quantity | Item | Function
4 | 100 mL glass thermal cores | Comparable test vessels
4 + 1 | Digital probe thermometers | Core and bath measurements
1 | Bucket or deep container | Cold bath and secondary containment
1 set | Cotton, bubble wrap and Mylar | Four insulation configurations
As needed | Tape or elastic bands | Repeatable assembly without compression
1 set | Gloves or tongs, towels and timer | Safe handling, cleanup and timing
1 | Adult-controlled hot-water source | Prepare water near 80 °C
Per student | Task sheet or laboratory report | Hypothesis, raw data and evaluation
Exact cost depends on local sourcing. The older €35.20 estimate remains an unverified draft procurement figure.
Notes: Suggested timing: Backup
Use this slide only if the audience asks about kit contents, reuse or feasibility.
Handoff cue: Pause for the next speaker or section when the final point lands.
Sources:
- Engineering Project Report, Section 10
- Thermal Insulation SOP, Hardware Checklist

## Slide 16
APPENDIX
Appendix: 12-step operating procedure
SPHERE THERMAL INSULATION LABORATORY
16
01
Prepare a stable, dry work area.
02
Measure and record the bath temperature.
03
Label the four test conditions.
04
Build each package without compressing its layers.
05
Prepare water near 80 °C under adult supervision.
06
Condition the thermal core to 80 ± 2 °C.
07
Transfer with gloves or tongs; keep probe depth fixed.
08
Start timing immediately and record T₀.
09
Record one temperature every minute through t = 15.
10
Repeat with the same geometry, mass and method.
11
Calculate drop, residuals, MAE and fitted k as required.
12
Cool, dry and store all equipment safely.
Notes: Suggested timing: Backup
This is the condensed presenter version of the complete SOP. Emphasize steps 5–7 when discussing hot-water handling.
Handoff cue: Pause for the next speaker or section when the final point lands.
Sources:
- Thermal_Insulation_SOP.docx
- Experimental_Toolkit_Thermal_Insulation_SOP_Illustrated.docx

## Slide 17
APPENDIX
Appendix: complete observed temperature series
SPHERE THERMAL INSULATION LABORATORY
17
Time (min) | Full MLI (°C) | Bubble (°C) | Mylar (°C) | Bare (°C)
0 | 77.6 | 82.6 | 80.5 | 80.1
1 | 76.6 | 79.0 | 68.6 | 73.9
2 | 76.1 | 75.2 | 61.8 | 66.0
3 | 75.6 | 72.5 | 55.8 | 59.9
4 | 75.1 | 70.0 | 51.3 | 54.5
5 | 74.5 | 67.9 | 47.8 | 50.1
6 | 73.9 | 65.6 | 44.9 | 47.1
7 | 73.5 | 64.0 | 42.5 | 44.6
8 | 72.1 | 62.3 | 40.6 | 42.5
9 | 70.6 | 60.6 | 38.9 | 40.9
10 | 69.7 | 58.9 | 38.1 | 39.5
11 | 68.5 | 57.5 | 36.3 | 38.2
12 | 67.4 | 56.1 | 35.5 | 37.3
13 | 65.8 | 54.8 | 34.6 | 36.5
14 | 64.1 | 53.7 | 33.9 | 35.8
15 | 62.7 | 52.6 | 33.3 | 35.2
Notes: Suggested timing: Backup
Use this slide to answer questions about individual readings or to verify the plotted series.
Handoff cue: Pause for the next speaker or section when the final point lands.
Sources:
- Engineering Project Report, Section 8
- Thermal Insulation SOP, Table 7

## Slide 18
APPENDIX
Appendix: model agreement and fitted cooling constant
SPHERE THERMAL INSULATION LABORATORY
18
Residual at point i
Residualᵢ = Tmeasured,ᵢ − Tmodel,ᵢ
Shows the signed difference at one timestamp
Mean absolute error
MAE = (1/n) Σ |Residualᵢ|
Summarizes the typical absolute temperature error
Fitted cooling constant
k = −ln[(T(t) − Tenv)/(T₀ − Tenv)] / t
Valid only when the ratio is positive and the boundary is stable
Normalized heat retained
(T₁₅ − Tref)/(T₀ − Tref) × 100%
Supports comparison when starting temperatures differ
The Mission Control full-MLI screenshot uses the supplied 16-point series and reports MAE = 0.98 °C against the 80/0 °C reference curve.
Notes: Suggested timing: Backup
Explain why MAE is easier to interpret than signed average error: positive and negative residuals cannot cancel. A fitted k is a system-level estimate for the tested boundary and geometry.
Handoff cue: Pause for the next speaker or section when the final point lands.
Sources:
- README.md
- Engineering Project Report, Section 9
- app.js, telemetry calculation

## Slide 19
APPENDIX
Appendix: unified assessment and classroom guidance
SPHERE THERMAL INSULATION LABORATORY
19
TEN ALIGNED QUESTIONS
Student Task Sheet: Inquiries 1–10
Mission Control: Questions 1–10
Teacher Manual: complete solution key
Nine multiple-choice items auto-score online
Question 4 requires instructor review
Assessment focuses on mechanism, modelling, fair testing, uncertainty and spacesuit engineering trade-offs.
Safety disclosure: the activity does not certify materials for aerospace, pressure-vessel, fire-protection or personal-protective use.
Notes: Suggested timing: Backup
Use this slide for questions about marking and learning verification. Question 4 remains open response because students must identify plausible physical causes of model deviation.
Handoff cue: Pause for the next speaker or section when the final point lands.
Sources:
- Teacher Manual, Assessment Guide
- index.html, Question Sheet
- README.md